## Slide 1: Internet of Things Starter Workshop
Danil Borchevkin
Danil.Borchevkin@Lab409.ru
+79114692217
Kaliningrad
2018

## Slide 2: Who am I?
Danil Borchevkin;
28 years;
Married;
Master of EE (IKBFU, 2014);
Owner Lab409 LLC;
More a engineer than businessman =((
Main skills – Electrical Engineering, PCB Design, Firmware Engineering, Electronic Design.
Points of interest: RF, ARM, MSP43x, Tiva C, EFM32, STM32, Cloud-backends

## Slide 3: Part 1 What is IoT exactly
#history #technology #peoples

## Slide 4: Evolution of Industry

## Slide 5: History of IoT
198x – D2D conception.
1990 – first connected thing – a toster with embedded TCP/IP abilities.
1990 – several guys in Sun Microsystems start develop new language for embedded systems.
199x – M2M expansion (POS, ATM, banking).
1999 – IoT named IoT by Kevin Ashton (MIT, Auto-ID) during presentation for Procter & Gamble (RFID for logistics).
2004 – article in Scientific American about IoT conception.
2008 – USIC named IoT one of six dangerous technologies.
2009 - borning of IoT – amount of things exceeded people’s population.
2011 - Gartner named Iot as «tech trigger» with 10 years time of shaping.

## Slide 6: M2M is a complex of techs but not a concept
Machine-to-Machine, M2M is a common name of technologies which purposed to machine connect with other machine (simplex/duplex):
Secuirity systems.
POS.
ATM.
Vending.
Fleet tracking.
Main techs: GSM/GPRS, GNSS (GPS, Galileo, Glonass and so on), Wired/Wireless common and industry-specific protocols.

## Slide 7: IoT is a conception but not a technology
IoT is a conception of network consist of physical objects(«things») which enable these objects to collect and exchange data. The IoT allows objects to be sensed or controlled remotely across existing network infrastructure creating opportunities for more direct integration of the physical world into computer-based systems, and resulting in improved efficiency, accuracy and economic benefit in addition to reduced human intervention.
IoT based on:
Embedded systems (electronics+firmware+mechanics+optics+chemistry)
Connectivity (Wired and Wireless protocols and high-level protocols).
M2M.
Internet.
Data analytics.

## Slide 8: IoT is a… infrastructure. A network of networks
"Instruct the children not to dream of toys or sweets. Instruct them to dream of infrastructure." Vadim Kozlov, Axioms from the Minutes of the Central Directorate
Civilization. Beyond the Earth

## Slide 11: Part 2 Ground Level of IoT
#embedded #things #connectivity

## Slide 12: Some theory

## Slide 13: Embedded systems
Typical embedded system consist of:
Electronics;
Firmware;
Chemical things;
Mechanical things;
Optical Things.
“Thing” is embedded system with M2M abilities (wired/wireless protocol)

## Slide 14: Connecting ways
IoT not mean what all things have direct internet connection.
Many things have to connect to cloud over gateways and adaptation servers.
It’s all about economy and processing issues.

## Slide 15: Wired protocols (low-levels)
Ethernet;
RS-422;
RS-485;
Fiber Optics;
CAN;
And Industry-specific.

## Slide 16: Wireless protocols (all levels)
Out of category – all types of barcodes;
RFID/NFC;
Bluetooth (Classic and Smart);
802.11 based – WiFi, etc;
802.15.4 based noIP – ZigBee, etc;
802.15.4 IP-based – 6loWPAN – Thread, etc;
Proprietary RF in 2.4 GHz
Proprietary RF in ISM (Sub 1GHz) – 433, 868/915 MHz – Z-Wave, etc;
GSM/GPRS 2G/3G/4G/5G;
Latest WAN – LoRA, NB-IoT, SigFox.

## Slide 17: Barcodes

## Slide 18: RFID/NFC

## Slide 19: Bluetooth

## Slide 20: ZigBee – 802.5.14 most popular protocol

## Slide 21: 6loWPAN and based on it. Thread

## Slide 22: About protocols

## Slide 23: What engineers think about IoT

## Slide 24: Part 3 Cloud services for IoT
Do Internet of Things but not a Thing-in-itself

## Slide 25: How clouds implement systems for IoT

## Slide 26: Popular IoT clouds

## Slide 32: Some issues in Russia
No alternatives to GSM/GPRS (upd. NB-IoT is coming) as a WAN;
Customs issues;
“Strange” logistic;
“Russian business”;
High prices of components, devkits;
There are no Russian competitors on a microelectronic market;
Availability of new components (domestic resellers): +1 year from release.

## Slide 33: Part 3 Labs
#lab #mediatek #OpenWRT

## Slide 34: Core of your “thing” – MediaTek LinkIt Smart 7688
OpenWRT
Single input single output(1T1R) Wi-Fi 802.11 b/g/n.
Pin-out for GPIO, I2C, I2S, SPI, UART, PWM and Ethernet Port.
580 MHz MIPS CPU.
32MB flash and 128MB DDR2 RAM.
USB host.
Micro SD slot.

## Slide 35: Grove actuators and sensors
150+ ready sensors and actuators
Ready code and examples for main platforms
No PCB development and soldering needed
Good to quick start and PoC

## Slide 36: Software
Your “thing” has a OS OpenWRT. It’s a good news for start!
For your “thing” you can write code on high-level languages – Python, Node.JS, Lua…
For own workshop we will use free cloud backend dweet.io with visualizing tool freeboard.io
As we have OS so we can connect to own “thing” by SSH

## Slide 37: Lab 01 - Blink
Your script placed at ~/ws_iotstarted/lab01/lab01.py
Change directory by cd command
Open the script by nano
Following instruction in the code
Then exit from nano by pressing Ctrl+X
Run code by ./lab01.py
If you want to exit from script press Ctrl+C
Finish!

## Slide 38: Lab 02 – First sensor
Your script placed at ~/ws_iotstarted/lab02/lab02.py
Change directory by cd command
Open the script by nano
Following instruction in the code
Then exit from nano by pressing Ctrl+X
Run code by ./lab02.py
If you want to exit from script press Ctrl+C
Finish!

## Slide 39: Lab 03 – Send data to cloud
First – finish registration on http://freeboard.io
Your script placed at ~/ws_iotstarted/lab03/lab03.py
Change directory by cd command
Open the script by nano
Following instruction in the code
Then exit from nano by pressing Ctrl+X
Run code by ./lab03.py
If you want to exit from script press Ctrl+C
Go to http://dweet.io and verify data ingestion
Go to http://freeboard.io and build your dashboard
Finish!

## Slide 40: Lab 04 – Be connected
Show your soft-skills – if you have sensor find another participant with actuator and vice verca
Your script placed at ~/ws_iotstarted/lab04/lab04_actuator.py or ~/ws_iotstarted/lab04/lab04_sensor.py (depence from your “thing”)
Change directory by cd command
Open the script by nano
Following instruction in the code
Then exit from nano by pressing Ctrl+X
Run code by ./lab04_sensor.py or ./lab04_actuator.py
If you want to exit from script press Ctrl+C
Finish!

## Slide 41
Danil Borchevkin
+7 911 469 22 17
Danil.Borchevkin@Lab409.ru
Lab409.ru